## Slide 1: OneDM@WoT Plugfest
Summary
Michael J. Koster

## Slide 2: Goals
Explore SDF => TM/TD Generation
Define how SDF semantic annotation works
Test the Modbus protocol binding

## Slide 3: SDF to TM Conversion
Inserted WoT DataSchema and Forms construct into SDF as extensions
Created an sdfThing that customizes its sdfObject components and inserts the WoT extensions
Generated a TD manually from this file:
https://github.com/mjkoster/onefb-sdk/blob/main/control-models/modbus/modbus-rtu.td.jsonld
TBD Create a set of transformation rules/handlers
Extend the conversion tool and framework
  Read Input => Invoke Transforms => Write Output

## Slide 4: Semantic Annotation using SDF
SDF URIs have json-pointer fragments
application/sdf+json contentType needs to be indicated where SDF is referenced
"@type": {
"https://onedm.org/playground/#/sdfObject/Voltage",
"contentType": "application/sdf+json"
}
Semantic annotation for sdfObjects using "links" construct in the TD, since there is no TD Object class
  We need a link relation like "implements" to describe this pattern

## Slide 5: TD Vocabulary – value scaling
We need to represent the data pattern which encodes a fixed point decimal number using an integer
Also other similar use cases where a liner re-scaling is needed
scaleMinimum and scaleMaximum are proposed for SDF
we could also consider unitMinimum and unitMaximum to make it clear that we are scale converting the raw number to the defined units

## Slide 6: Value Scaling (contd)
{
"type": "number",
"unit": "V",
"minimum": 0,
"maximum": 1200,
"multipleOf": 1,
"scaleMinimum": 0,
"scaleMaximum": 120000
}
The JSON validator works on the raw values and the application applies a linear scale interpolation
This is how the node-red value scaling node works
We also need other types of scale

## Slide 7: Modbus binding
Hosted 2 modbus devices for the test case and plugfest
Modbus vocabulary suggestions
  use address and quantity instead of offset and length
  review "entity" concept to collapse read/write/obs
Modbus URI construction feedback
Modbus requires read multiple entities
  Should we use array property or TD readmultiple?
  Entity blocks need to be defined separately in the TD
  Entity size needs to be defined in a dataschema extension
  How do we semantically identify the individual entities?