## Slide 1: One Data Model Semantic Definitions for Connected Things
T2TRG – WoT Workshop on IoT Semantics @IETF 106
November 14, 2019

## Slide 2: What is One Data Model?
A loose organization of SDOs, Device vendors, IoT Platform operators, and IoT experts
Goal is to harmonize IoT semantic models across SDOs and vendors
Heavy participation from connected home sector
Initially – a common "language" for IoT semantic models, usable by application domain experts
Eventually - convergence of semantic definitions for common IoT device types, broad adoption of the language

## Slide 3: History
Emerged from Zigbee "Hive" meeting, fall 2018
Cross-industry consensus on lack of common IoT data models as a key inhibitor to IoT growth
Broad industry group of SDOs and vendors
No legal organization – working under a liaison
Weekly teleconferences, 4 face to face meetings, in 2019
Working in a github repository
Language, tools, and models

## Slide 4: Process
Create a common representation language for existing IoT data and interaction models
  Enable contribution of the best existing models across all participating organizations
Collect a set of representative models for a "pressure test" of the language
  Convert to the new language and note any gaps
Organizations contribute models for evaluation
  Process for selecting a single model per function, e.g. lighting, door lock, thermostat
Publication of selected models

## Slide 5: Status
Weekly technical meetings since December 2018
Four face to face meetings
Diverse models are being used to test the language
At the October 2019 Face to Face meeting we approved a version of the modeling language to proceed with contributions
  SDF - Simple Definition Format
Set up an area for contributions to be uploaded and evaluated

## Slide 6: Outcomes
All participants have agreed to publish the models under the BSD 3-Clause Open Source license
2-way translation between OMA LWM2M XML models and the SDF language
SDF models for Dotdot thermostat and lighting clusters are in progress, energy clusters next
SDF models for OCF appliances are in progress
OCF may use the SDF language as the "entry point" for developers to create and maintain data models
  Automatic mapping to OCF styled Swagger definitions

## Slide 7: What is a semantic model – Practical IoT Semantics
Abstract meta-model for IoT device affordances, behavior, and context
  Decoupled from network bindings, protocol-agile
  Common categories for affordances
  Common categories for constraints
  Common format for definitions
Initial focus on affordances to normalize device-facing interactions across SDOs and vendors
Behavioral and contextual models also are needed but not in the initial scope

## Slide 8: ODM Architecture
Meta-model
ODM Classes
  odmData
  odmProperty
  odmAction
  odmEvent
  odmObject
  odmThing
  odmView

## Slide 9: ODM Meta-Model
Thing Class to compose Objects
View (Interface) Class to virtualize affordances
Reusable Objects
  Property, Action, and Event Affordances
Reusable Data Types

## Slide 10: odmProperty
Elements that represent the state of a connected thing – direct affordance to instances of Data Types
Read and Write meta-operations on Data elements
Read meta-operation returns the representation of state
Write meta-operation uses a supplied representation to update state
For example, the operational mode of a thermostat

## Slide 11: odmAction
Affordance, usually to control a physical world effector that is associated with a connected thing
Also emulates function calls
Invoke meta-operation with zero or more input data parameters
Output data returns information including status of long running actions
E.g. locking or unlocking a door lock

## Slide 12: odmEvent
An affordance to obtain happenings associated with the connected thing, often to receive asynchronous or unsolicited notification messages
Subscribe meta-operation to map to most protocols, e.g. CoAP Observe, MQTT Subscribe, HTTP long poll or eventSource
Could be notifications of state changes, also alerts and alarms
Output data contains state or application messages

## Slide 13: odmData
Reusable definitions for data types – JSON Schema
May use the same odmData definition for odmProperty as for odmAction input data, odmEvent output data
Defines a semantic type, e.g. temperatureData, and basic data type (number, string, boolean), with additional constraints (enum, minimum, maximum, number of decimal places, etc.), and associations with quantities and units
Well known types for date, time, URL, UID, etc.

## Slide 14: odmObject
A collection of Properties, Actions, and Events
Work together to perform some discrete function
On/off switch, light dimming, color control, door lock/unlock
odmObject is the main point of commonality for interoperability
Similar functional odmObjects have similar affordances
Defines minimum required set of affordances

## Slide 15: odmThing
A collection of odmObjects and odmThings that work together in a complementary way
A light control thing may have on/off switch control, dimming control, and color control objects
A product thing may have several light things and other types of things, allowing for nested modular composition patterns

## Slide 16: odmView (Interface)
odmView is for defining virtual interfaces to a thing
For example, an interface may have limited functionality traded off for small data size over the air
odmViews are composed of odmObjects and odmThings that are defined elsewhere in the model, with additional qualities to constrain and define the behavior of the interface

## Slide 17: SDF Language Design Review
Overview – Functional structure
Definitions and Declarations
References using JSON Pointer
Processing model – namespaces and files
High Level Composition

## Slide 18: SDF Design Overview
JSON based DSL – JSON Schema validation
Associates semantic terms with type definitions of ODM classes
Example odmObject definition for a simple binary (on/off) switch control
  The odmObject for "Switch" object has three affordances:
  odmProperty for state "value" with a defined string enum allowing "on" and "off" values
  odmActions for "on" and "off" (that implicitly act on the "State" Property)

## Slide 19: SDF - Simple Definition Format
{
"info": {
"title": "Example file for ODM Simple JSON Definition Format",
"version": "20190404",
"copyright": "Copyright 2019 Example Corp. All rights reserved.",
"license": "http://example.com/license"
},
"namespace": {
"st": "http://example.com/capability/odm#"
},
"defaultNamespace": "st",
"odmObject": {
"Switch": {
"odmProperty": {
"value": {
"type": "string",
"enum": ["on", "off"]
}
},
"odmAction": {
"on": {},
"off": {}
}
}
}
}

## Slide 20: Simple example – Info and namespace definitions
"info": {
"title": "Example file for ODM Simple JSON Definition Format",
"version": "20190404",
"copyright": "Copyright 2019 Xcorp, Inc. All rights reserved.",
"license": "http://example.com/license"
},
"namespace": {
"ocf": "http://example.org/ocf/odm",
"st": "http://example.com/capability/odm"
},
"defaultNamespace": "st",
curies resolved
File Information
keywords

## Slide 21: Definitions
"odmObject": {
"Switch": {
"odmProperty": {
"value": {
"type": "string",
"enum": ["on", "off"]
}
},
"odmAction": {
"on": {},
"off": {}
}
}
}
SDF keywords
Terms defined in the Default Namespace

## Slide 22: Definitions
A definition consists of a defined term and a map of it's defined qualities
JSON Schema syntax is used for odmProperty and odmData constraint qualities
"value": {
"type": "string",
"enum": ["on", "off"]
}

## Slide 23: Declarations
A Declaration in SDF is some use of a defined term
Usually in another definition, through reuse of definitions
A declaration can also be an inline definition, within another definition
In the above example, "value" is a definition with its own declared qualities, as well as a declaration within the "Switch" definition
Are statements about qualities in a definition also declarations?

## Slide 24: SDF References
The defined qualities, and the semantic identity, of a definition can be re-used in a new definition
For example, a common definition for Transition Time Data can be used for timing parameters of different Actions in a lighting control model
Reuse of definitions in SDF models is achieved through references, using JSON Pointer (RFC6901)
Some examples use JSON Relative Pointers (I-D)

## Slide 25: odmRef keyword
Functions in a similar way as #ref in JSON schema
Can be thought of as copying the qualities of the referenced definition into the current definition
Additional qualities may be defined, e.g. semantic tagging, in the current definition

## Slide 26: odmRef Example
"odmData": {
"transitiontimedata": {
"type": "number",
"widthInBits": 16,
"minimum": 0,
"maximum": 65535,
"multipleOf": 1,
"unit": "seconds",
"scaleMinimum": 0,
"scaleMaximum": 6553.5
}
}
"OnOffTransitionTime": {
"odmRef": "#/odmData/transitiontimedata",
"name": "On Off Transition Time",
"default": 0
},
Definition
Declaration

## Slide 27: Processing Model – Files and Namespaces
Multiple SDF files are expected to be submitted to populate a namespace
The defaultnamespace declaration in each SDF file determines the destination namespace location of the definitions that are in the file
Lookup operations on the namespace will behave as if there is one file that contains all of the definitions in that namespace
Accepting a definition file into a namespace is agreeing to roll it into the single file image

## Slide 28: Data Type Definition
{
"info": {
"title": "Example ODM Data Type definition",
"version": "20190504",
"copyright": "no copyright",
"license": "not licensed"
},
"namespace": {
"zcl": "http://example.com/zcl/odm#"
},
"defaultnamespace": "zcl",
"odmData": {
"transitiontimedata": {
"type": "number",
"widthInBits": 16,
"minimum": 0,
"maximum": 65535,
"multipleOf": 1,
"unit": "seconds",
"scaleMinimum": 0,
"scaleMaximum": 6553.5
}
}
}

## Slide 29: Example use of definition from a namespace
"namespace": {
"zcl": "http://example.com/zcl/odm#"
},
"MoveToTiltTransitionTime": {
"odmRef": "zcl:odmData/transitiontimedata",
"name": "Move To Tilt Transition Time",
"default": 0
},
Reference doesn't need to know about file names or how a definition was contributed
Namespace prefix in the reference is expanded to a URL prefix before JSON Path processing

## Slide 30: Other use of JSON Pointer in SDF
Indicate sub-sets of definitions that are required or designated as input or output data
"odmAction": {
"MoveToLevel": {
"name": "Move to Level",
"odmRequired": [
"0/odmData/level",
"0/odmData/transitiontime"
],
"odmInputData": [
"0/odmData/level",
"0/odmData/transitiontime"
],
"odmData": {
"level": {
"name": "Level",
"type": "number",
"widthInBits": 8,
"minimum": 0,
"maximum": 254
},
"transitiontime": {
"name": "Transition Time",
"odmRef": "#/odmData/transitiontimedata"
}

## Slide 31: High Level Compositions
odmThing
  Contains definitions of odmObjects and, recursively, odmThings
odmView (Interface)
  Models a set of already-defined odmObjects and odmThings that are composed into a virtual interface
  Defined within an odmThing, can only refer to other elements defined or declared within the odmThing in which the odmView is defined
  Can define overlapping or disjoint functional subsets of an odmThing, or expose specialized representations for compactness, privacy, etc. – e.g. a read-only view

## Slide 32: Thing Example
"odmProduct": {
"SKU_19934774": {
"productTypeListing": "Compound Vacuum Gauge",
"required": [
"0/odmObject/3300~10"
],
"odmObject": {
"3300/0": {
"odmRef": "#/odmObject/genericSensor",
"odmProperty": {
"minimumRange": {
"const": -120000
},
"maximumRange": {
"const": 120000
},
"applicationType": {
"const": "Vacuum Gauge"
},
"sensorType": {
"const": "absolutePressure"
},
"units": {
"const": "Pa"
}

## Slide 33: odmView Example
"odmView": {
"oic.if.s": {
"isDefaultView": true,
"odmComponent": [
"#/odmObject/oic.r.temperature/odmProperty/temperature",
"#/odmObject/oic.r.temperature/odmProperty/units"
]
},
"oic.if.a": {
"odmComponent": [
"#/odmObject/odmProperty/temperature",
"#/odmObject/odmProperty/units"
]
},
"oic.if.rw": {
"odmComponent": [
"#/odmObject/odmProperty/temperature",
"#/odmObject/odmProperty/units",
"#/odmObject/odmProperty/range",
"#/odmObject/odmProperty/step",
"#/odmObject/odmProperty/precision"
]
},

## Slide 34: Next steps
More updates to the language in progress
Model convergence across vendors, SDOs
Demonstration based on translation and gateway
Public announcement soon, timing discussion
Semantic Proxy project – W3C WoT integration

## Slide 35: Semantic Proxy – W3C Web of Things Integration
"Thing Description" associates semantic identifiers for Properties, Actions, and Events with affordance descriptions consisting of data schemas and protocol bindings
Protocol bindings associate network operations with meta-operations in the semantic model
"Incoming" Consumed TD and "Outgoing" Exposed TD have the same affordances in the semantic model, and customized data schemas and protocol bindings

## Slide 36: Semantic Proxy - Schematic
Semantic Proxy
WoT Servient
OCF Application
IPSO Dev
IPSO Dev
Cons. TD
Exp.
TD
Exposed Thing TDs have OCF protocol binding
Consumed Thing TDs have IPSO protocol binding
Both TDs have the same meta interactions and operations defined in OneDM models

## Slide 37: Semantic Proxy – RDF Converter
Create RDF statements from OneDM definitions for use in semantic tooling
iotschema style RDF definitions are aligned with the meta-model
WoT Thing Description can use iotschema definitions for annotation
  WoT TD only has Thing and affordance (P/A/E) classes
odmObject maps to iotschema Capability
odmThing and odmView don't directly map but can extend iotschema Capability

## Slide 38: References
One Data Model SDF and Model work in progress
https://github.com/one-data-model/language
https://github.com/one-data-model/playground
Semantic Proxy and W3C WoT
https://github.com/tum-ei-esi/virtual-thing
https://www.w3.org/TR/2019/CR-wot-thing-description-20191106/
https://www.w3.org/TR/2019/CR-wot-architecture-20191106/