## Slide 1: ODM Extensions for Complex and Composed Definitions
One Data Model
June 14, 2019

## Slide 2: Updates
Don't need to use Include + Type
odmThing has more potential scope
enum pattern

## Slide 3: The Problem
How to represent complex things while retaining the atomic integrity of Object definitions
  Compositions that can represent modular products
  Constraints that apply to standardized product types
  Reuse definitions of Objects and standardized Object compositions
  Ability to set qualities like units, range, and scale on a product or product type basis
  Ability to create specialized "Views" into the functionality of a product or product type

## Slide 4: Illustrative Examples
A power strip with some number of individually controllable plugs
  A plug is composed of on/off control, energy monitor, and dimming Objects
  There is an Object that controls and monitors power on all plugs
A multifunction printer + scanner product
  Printing and scanning are separately controlled
  Main power can be controlled by either printer or scanner controls
Reusable definitions

## Slide 5: Use case categories
Define a reusable composition of odmObjects that work together to provide a function
  odmThing
Define a mandatory set of Objects, Qualities, and settings for interoperability like Device Type
  also odmThing?
Define a specific product configuration, ability to model the composition of a SKU level entity.
  composed of Objects and Things
  odmProduct

## Slide 6: Design Elements
Path construction in models and definitions
Re-use and Recursion
  "type"
  "include"
Composed types
  odmThing (a composition of objects with optionality)
  odmProduct (also a thing, but has specific qualities and optionality, represents a SKU)
  odmView (an element, may only include references to instances of objects, properties, events, and actions)

## Slide 7: Path Construction in a Definition
{
"namespace": {
"st": "http://example.com/capability/odm"
},
"defaultNamespace": "st",
"odmObject": {
"Switch": {
"odmProperty": {
"value": {
"type": "string",
"enum": ["on", "off"]
}
},
"odmAction": {
"on": {},
"off": {}
}
}
}
}
#/odmObject/Switch or st:/odmObject/Switch
#/odmObject/Switch/odmProperty/value
#/odmObject/Switch/odmAction/on
#/odmObject/Switch/odmAction/off

## Slide 8: JSON Pointer Namespace Prefix
Add a namespace prefix to JSON Pointers used to identify model elements in different files
The namespace prefix may be used in place of document paths in a filesystem
Cross-document paths start with the namespace prefix
"namespace": {
"ex": "https://example.com"
}
JSON pointer expression "ex:/odmObject/temperature"
Expands to "https://example.com/odmObject/temperature"

## Slide 9: Re-use and Recursion
type
  Use an existing definition as a type for a new definition
  "type": { "$ref": "#/odmData/temperatureData" }
include
  Include an existing definition (instance) in this context
  "include": [ { "$ref": "#/odmObject/PowerStateControl" } ]
include + type
  Use an existing definition, including its name, in a new definition in the current context (IPSO style re-use)
  "include": [ { "type": { "$ref": "#/odmProperty/sensorValue" } } ]

## Slide 10: type
use an exsiting definition as a template for a new definition
"odmObject": {
"3300/0": {
"type": {
"$ref": "#/odmObject/genericSensor"
},
"optional": false,
"odmProperty": {
"OnOffTransitionTime": {
"type": {
"$ref": "#/odmData/transitiontimedata"
},

## Slide 11: To re-use a named definition
To re-use a named definition, as in IPSO Smart Objects, simply duplicate the name. The ID will be the same as the linked definition
"odmObject": {
"genericSensor": {
"id": 3300,
"odmProperty": {
"sensorValue": {
"type": {
"$ref": "#/odmProperty/sensorValue"
}
},
(...)

## Slide 12: include
Include an instance of an ODM element from another part of the definition
"odmView": {
"sensor": {
"include": [
{
"$ref": "#/odmObject/temperature/odmProperty/temperature"
},
{
"$ref": "#/odmObject/temperature/odmProperty/units"
}
]
},

## Slide 13: Composed Types
odmThing
  Encapsulates a set of odmObjects and selects optionality
  May extend definitions and add new definitions
  "Device Type" specification
odmProduct
  Product, composed from standardized functionality
  Encapsulates Objects and Components and selects optionality
  May extend and add new definitions
odmView
  Consists a set of elements that use the include pattern to create a view of instances of elements

## Slide 14: Questions and Issues
odmView is just an odmThing that only references other instances of odmThing and odmObject – can we just use odmThing?
odmThing can contain odmThing – for example, the OCF collection pattern in oic.r.airflowcontrol
Do we agree on the pattern for defining enums that includes both string and number?
{
"type": "object",
"enum": [ {"run": 1}, {"stop": 2}, {"jog": 3} ]
}

## Slide 15: Examples
type – ZCL level model that has multiple timers
named type – ipso 3300 Object model that reuses definitions of odmProperties
odmProduct – ipso model of a vacuum gauge with two specialized 3300 type sensor Objects
odmView – a definition of an OCF interface

## Slide 16: Issue – Name vs. JSON tag
Our definition format allows the following
"odmProperty": {
"onOffState": {
"name": "onOffState",
"id": 3
}
}
The JSON tag is the definition and the reference

## Slide 17: Issue – Use of oneOf outside schemas
"odmProperty": {
"temperature": {
"oneOf": [
{
"type": "number",
"name": "value",
"id": 1
},
{
"type": "number",
"enum": [1,2,3,4],
"name": "index",
"id": 2
}

## Slide 18: Issue - Nullability
We allow "nullability"as a quality, meaning that the value (property or data parameter) can be represented as a null value
Null value representation is serialization dependent and includes many ad-hoc schemes such as reserved values
JSON null is both a type and a value
We need to allow null, so may define an implicit "oneOf" in the schema for nullable values to enable a default JSON implementation

## Slide 19: Full examples
https://github.com/mjkoster/ODM-Examples/blob/master/tdl/level.sdf.json
https://github.com/mjkoster/ODM-Examples/blob/master/tdl/ocf-example.sdf.json
https://github.com/mjkoster/ODM-Examples/blob/master/tdl/ipso3300.sdf.json